## Slide 1: Enhancing Input On and Above the Interactive Surface with Muscle Sensing
Hrvoje Benko, T. Scott Saponas, Dan Morris, and Desney Tan
Microsoft Research and University of Washington
ACM ITS 2009

## Slide 2: Touch Sensitive Interfaces
Problems:
  Contact identification
  Pressure sensing
  Above the surface sensing
  - gloves, Visual Touchpad
  - FTIR, FSR
  - SecondLight, DepthTouch
Notes: TODO redo this slide a bit

## Slide 3: Our Approach

## Slide 4: Sensing Muscle Activation
Electrical signal can be sensed by Electromyography (EMG)
Notes: nervous system, motor neuron, action potential, muscle fiber
For those of us who are not biology or medical experts here is a quick primer on muscles and muscle sensing
There are muscles for breathing and heartbeat
And then there are muscles we use for locomotion, and those are what we are talking about using in muscle-computer interfaces
The neurological signal for muscle activation can be sensed at the surface of the skin, and we want to make use of this type of physiological sensing for computer input.

## Slide 5: Related Work
Jacobsen, et al. “Utah Arm”, ‘74
Costanza, et al. “Intimate interfaces in action”, CHI ‘05
Wheeler & Jorgensen “Neuroelectric joysticks”, ‘02
Naik, et al. “Hand gestures”, ‘07
Notes: 1890 the term electromyography introduced
Closely related to EEG – electroencephalography

## Slide 6: Related Work
Saponas et al., CHI ‘09
Saponas et al., UIST’09
Offline
Real-Time

## Slide 7: Complimentary Modalities
Interactive Tabletops
Muscle Sensing
Easy
  Location and footprint of multiple contacts
Difficult
  Identification of contacts
  Sensing of pressure
  Sensing above the surface
Easy
  Sensing muscle activation
  Identifying muscles
Difficult
  Spatial location of body parts

## Slide 8: Our Equipment
BioSemi EMG
Monitor/Amplifier
Microsoft Surface
Forearm sensors

## Slide 9: Challenges in Sensing Fingers

## Slide 10: EMG Sensors & Data

## Slide 11: Stimulus Response Training

## Slide 12: Gesture Classification
30 millisecond sample
X 8 Sensors
Support Vector
Machine
labeled
training data
user specific model
machine learning
Notes: Standard Machine Learning Setup
Based on related work in EMG sensing and our previous work with EEG sensing we…
PER USER MODELS
figures showing data->features->training->model-> classification
For our experiment, we used the Sequential Minimal Optimization (SMO) version of support vector machines as implemented in the Weka toolkit
I’ve told you now that we put 8 sensors on people had them perform 4 gesture sets of 4-5 gestures each at least 50 times.
So what did we do with all this data?
We conducted offline analysis using techniques we decided upon before running the experiment

## Slide 13: Gesture Classification
30 millisecond sample
Root Mean Square (RMS)
ratios between channels
Frequency Energy
10 Hz bands
Phase Coherence
ratios between channels
X 8 Sensors
Features
Support Vector
Machine
labeled
training data
user specific model
machine learning
Notes: Standard Machine Learning Setup
Based on related work in EMG sensing and our previous work with EEG sensing we…
PER USER MODELS
figures showing data->features->training->model-> classification
For our experiment, we used the Sequential Minimal Optimization (SMO) version of support vector machines as implemented in the Weka toolkit
I’ve told you now that we put 8 sensors on people had them perform 4 gesture sets of 4-5 gestures each at least 50 times.
So what did we do with all this data?
We conducted offline analysis using techniques we decided upon before running the experiment

## Slide 14: Gesture Classification
30 millisecond sample
Root Mean Square (RMS)
ratios between channels
Frequency Energy
10 Hz bands
Phase Coherence
ratios between channels
X 8 Sensors
Features
Support Vector
Machine
user specific model
machine learning
gesture
classification
Notes: Standard Machine Learning Setup
Based on related work in EMG sensing and our previous work with EEG sensing we…
PER USER MODELS
figures showing data->features->training->model-> classification
For our experiment, we used the Sequential Minimal Optimization (SMO) version of support vector machines as implemented in the Weka toolkit
I’ve told you now that we put 8 sensors on people had them perform 4 gesture sets of 4-5 gestures each at least 50 times.
So what did we do with all this data?
We conducted offline analysis using techniques we decided upon before running the experiment

## Slide 15: EMG + Surface Interactions

## Slide 16: Pressure Sensing

## Slide 17: Finger Identification

## Slide 18: Off-Surface Interactions
Undo

## Slide 19: Off-Surface Interactions
Pinch & Throw

## Slide 20: UI Considerations
Dealing with lag
  Classification lag:
    Pressure (<150ms)
    Finger ID (<300ms)
    Hand flick (<50ms)
  Our guideline:
    Instantaneous response
    Fill missing details ASAP

## Slide 21: UI Considerations
Finger-dependent UI elements
Pre-sense visualizations

## Slide 22: Pilot Experiment
6 participants (3F, 3M)
90 min sessions
Five tasks
  Copy images with pressure-sensitive painting
  Copy images with finger-dependent painting
  Draw alternating vertical lines
  Draw plus undo alternate numbers
  Cut-copy-paste images between 2 canvases

## Slide 23: Experiment Results
Confirmed feasibility of our approach
Across tasks/participants accuracy >90%
  1 participant ~ 75% accuracy for finger ID
Participants

## Slide 24: Limitations
Per user/per session calibration
Training method is critical
90% might not be good enough
Single contact at the time
Not all fingers are created equal
Bulky, expensive equipment
Notes: TODO

## Slide 25: Big Challenges
Wires
Sensors & Equipment
Training
Reliability/Repeatability

## Slide 26: Addressing the Challenges
A wireless, dry-electrode armband
Cross-session training

## Slide 27: Wireless EMG Armband

## Slide 28: Thank You
T. Scott Saponas Dan Morris Desney Tan
Graduating!
Hrvoje Benko
benko@microsoft.com

## Slide 29: Extras

## Slide 30: Sensor Stream